WI(R)-40~300(mm)

Horizontal vane wheel, dry-dial Irrigation(Seawage)cold (hot) water meter

Application:

--Measuring the total volume of cold(hot) water passing through the pipeline.

-NOTE:This type of water meter can be used for a remote reading transmission system as equipped with built-in-sensor.

Feature:

--Small transmission resistance,large flow capacity, anti-block and strong anti-pollution ability.

--Dry-dial, Magnetic drive;

--Vacuum sealed register ensures the dial keep free from condensation and keep the reading clear in a long term service;

--Removable measuring unit and strong universality, easy installation and maintenance;

--Remote transmission device can be added upon request,such as Reed Switch or Hall, Pulse Output:DN50-200mm 1000L/P、100L/P; DN250-300mm 10000L/P、1000L/P

--Technical data conform to international standard ISO 4064.

Working condition

Water temperature: T30 T50 T90 Water pressure class: MAP16  MAP10

Pressure-loss Class: △p63

Maximum permissible errors

(1) From minimum flow-rate(Q1) inclusive to transitional flow-rate(Q2) exclusive±5%.

(2) From transitional flow-rate(Q2) to overload flow-rate(Q4):±2%(Hot water meter ±3%)

MAIN TECHNICAL SPECIFICATIONS FOR COLD WATER

| Type | Size | Class | qs Overload Flow | qp Permanent Flow | qt Transitional Flow | qmin Min. Flow | Min. Reading | Max. Reading |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  | m3/h | m3 |
| WI-40 | 1½" | A | 30 | 15 | 4.5 | 1.2 | 0.0002 | 999,999 |
| WI-50 | 2" | A | 30 | 15 | 4.5 | 1.2 | 0.0002 | 999,999 |
| WI-65 | 2½" | A | 50 | 25 | 7.5 | 2.0 | 0.002 | 999,999 |
| WI-80 | 3" | A | 80 | 40 | 12 | 3.2 | 0.002 | 999,999 |
| WI-100 | 4" | A | 120 | 60 | 18 | 4.8 | 0.002 | 999,999 |
| WI-125 | 5" | A | 200 | 100 | 30 | 8 | 0.002 | 999,999 |
| WI-150 | 6" | A | 300 | 150 | 45 | 12 | 0.002 | 999,999 |
| WI-200 | 8" | A | 500 | 250 | 75 | 20 | 0.002 | 999,999 |
| WI-250 | 10" | A | 800 | 400 | 120 | 32 | 0.02 | 9,999,999 |
| WI-300 | 12" | A | 1200 | 600 | 180 | 48 | 0.02 | 9,999,999 |

### DIMENSIONS

| Type | Size | L Length | H Height | Connecting flange |
| --- | --- | --- | --- | --- |
|  |  |  |  | φD1 Outside diameter | φD2 Bolt circle diameter | Connecting Bolts (n-M) |
|  | mm |  |  |  |
| WI-40 | 1½" | 300 | 215 |  |  | R1½(螺纹连接） |
| WI-50 | 2" | 200 | 253 | 165 | 125 | 4-M16 |
| WI-65 | 2½" | 200 | 268 | 185 | 145 | 4-M16 |
| WI-80 | 3" | 225 | 284 | 200 | 160 | 8-M16 |
| WI-100 | 4" | 250 | 295 | 220 | 180 | 8-M16 |
| WI-125 | 5" | 250 | 310 | 250 | 210 | 8-M16 |
| WI-150 | 6" | 300 | 339 | 285 | 240 | 8-M20 |
| WI-200 | 8" | 350 | 382 | 340 | 295 | 8-M20(1.0MPa) |
|  |  |  |  |  |  | 12-M20(1.6MPa) |
| WI-250 | 10" | 450 | 438 | 395 | 350 | 12-M20(1.0MPa) |
|  |  |  |  | 405 | 355 | 12-M24(1.6MPa) |
| WI-300 | 12" | 500 | 488 | 445 | 400 | 12-M20(1.0MPa) |
|  |  |  |  | 460 | 410 | 12-M24(1.6MPa) |

NOTE: The flange dimension conforms to ISO7005-2:1988 standard. Order for products of special requirements is also accepted.

| WI40～300 HORIZONTAL VANE WHEEL, DRY-DIAL COLD WATER METER |
| --- |
| Code | Description | Material | QTY |
| 1 | Screw M5×45 For Sealing | Stainless Steel | 1 |
| 2 | Screw M5×45 | Stainless Steel | 1 |
| 3 | Cover With Lid | Assembly | 1 |
| 4 | Sealed Register | Assembly | 1 |
| 5 | Screw | Stainless Steel | 4 |
| 6 | Support | ABS | 1 |
| 7 | Bolt For Sealing M12×35 | Stainless Steel | 1 |
| 8 | Bolt M12×35 | Stainless Steel | 3 |
| 9 | Gasket | Stainless Steel | 4 |
| 10 | Adjusting Nut | Brass | 1 |
| 11 | Flange Plate | Cast Iron(or Nodular cast iron) | 1 |
| 12 | O-ring | Silicon Rubber | 1 |
| 13 | O-ring | Silicon Rubber | 1 |
| 14 | Bush For Adjustment | Brass | 1 |
| 15 | Upper Bearing Plate | Brass | 1 |
| 16 | PIVIT | Stainless Steel | 4 |
| 17 | Lower Central Gear | Component | 1 |
| 18 | Cover Plate | MPPO | 1 |
| 19 | O-ring For Adjustment | Rubber | 2 |
| 20 | Transmission Gear Component | Assembly | 1 |
| 21 | Adjusting Lever | Brass | 1 |
| 22 | Turbine | Component | 1 |
| 23 | Adjusting Plate | MPPO | 1 |
| 24 | Turbine shaft | Stainless Steel | 2 |
| 25 | Measuring Chamber | MPPO | 1 |
| 26 | Fixing Screw | Stainless Steel | 3 |
| 27 | O-ring | Rubber | 1 |
| 28 | Body | Cast Iron(or Nodular cast iron) | 1 |

-- LIANYUNGANG HYTTEN METER CO.,LTD.

Address: NO.8 Hanguo Industrial Development Zone,Luoyang village,Dunshang Town,Ganyu District, Lianyungang City.

Tel：0518-85907891         Fax：0518-85907892

Http：//www. hyttenmeter.com  E-mail：hytten@hyttenmeter.com